## Slide 1: What Is the Project about?
Introduction

## Slide 2
PLS HELP!
I am too tired!

## Slide 3
Now no more stress
For Farmers
AI will conquer the troubles of farmers.

## Slide 5: Smart Irrigation System
A Smart Plant Watering System

## Slide 6: Table of Contents 1. Introduction Aim 2. ESP32 Power of this module 3. Project Explanation Detailed Project Explanation 4. Conclusion Final Conclusion 5. References Reference Materials 6. Thank you Thank You

## Slide 7: What is the aim of the Project
Introduction

## Slide 8: What is the aim of the Project
The aim of the project is to help the farmers and the crops.
The Project also can be used at home as Plant Watering System.
This Project will display the values of Humidity, Climate Temperature, Soil Moisture Level and the Pump Status.
The ‘OLED DISPLAY’ Will display the details mentioned above.
The Values can also be seen in the cloud through website or an app, from anywhere from the world.
The only thing is that the entire project requires constant internet supply.
This is helpful for the Homemakers who are tired of watering the plants in their homes.
But for the farmers there is no internet supply, so they can use the OLED Display to view the Data of the Soil Condition, Humidity and the Temperature.
If the soil moisture is less, then the motor will automatically water the plants.

## Slide 9: Whom will it help the most
Introduction

## Slide 10: Whom will it help the most
This Project will help in Two Sectors:
Automatic Plant Watering System:
This will be used in homes where the plants will be watered automatically after the soil moisture decreases than the trigger level.
When the moisture level exceeds the trigger level it will start the pump motor and water the plants.
Smart Irrigation System
This will bee useful for the farmers for watering their plants automatically when there is rain the soil moisture increases and the pump motor ill not pump. But when there is no rain, the crops will receive water from nearby ponds by motorized/solenoid valve and from PVC Pipes water will flow and produce water to plants.
The Effort of farmers will decrease in this process.

## Slide 11: Why did we choose this Project.
Introduction

## Slide 12: Why did we choose this Project.
The main reason to choose this project is to help the people in their home to water their plants regularly.
To stop the global warming, the people have started plating some plants. But they are forgetting to water those plants regularly.
To stop this problem, this will monitor the plant’s soil water condition.
The another reason is that the farmers would have to roam in the sum and turn on the solenoid valve to water their crops, but with this device, it will water the crops automatically.
The efficiency of crop production will increase and the global warming will also be controlled in the near future if there were more plants.

## Slide 13: Introduction to ESP32
ESP32

## Slide 14: Introduction to ESP32
This Module is a powerful MICRO-CONTROLLER developed by Esspressif Systems. It is Cheap and it has wide range of Applications.
The Microcontroller Unit (MCU) of the ESP32 is a dual core Xtensa LX6 MCU, which operates up to 240 MHz
Having two cores, it is allowed for better multitasking and handling multiple process simultaneously.
One of the standout features is that, it has Built-in WI-FI and Bluetooth Module in it.
It supports 2.4GHz WI-FI and Bluetooth V4.2
This is the reason this makes this module suitable for IOT Projects.

## Slide 15: Advantages of this Module
ESP32

## Slide 16: Advantages of this Module
Low Power Consumption:
  The ESP32 is designed in such a way that it is power efficient.
  It also includes multiple power saving modes, such that it consumes less power even if it is Idle.
Security Features:
  It includes hardware accelerated encryptions (AES, SHA-2, RSA, etc.).
  It also includes secure boot, flash encryption and secure storage.
Development Environment:
  The ESP-32 can be programmed using Arduino IDE which makes easy to develop the projects.

## Slide 17: PIN Layout of ESP32
ESP32

## Slide 18: PIN Layout of ESP32

## Slide 19: Components Used in this Project
Project Explanation

## Slide 20: ESP32

## Slide 21: Soil Moisture Sensor

## Slide 22: DHT11 Sensor

## Slide 23: OLED Display

## Slide 24: Keyes Relay Module

## Slide 25: Pump Motor

## Slide 26: Breadboard

## Slide 27: Working of the Project
Project Explanation

## Slide 28: Circuit Diagram

## Slide 29: Pins Connection
Pins of Module to ESP32
OLED Display
SDA – D22
SCL – D21
DHT11 Humidity/Temperature Sensor
OUT – D13
Soil Moisture Sensor
A0 – D34
Keyes Relay
Signal – D26

## Slide 30: Working
The OLED Display will show the output of all the Sensors.
The Soil Moisture Sensor will take an analog input and sends it to the ESP32 Module.
The Module Communicates with the network and send the data to the cloud.
Those Values are displayed in the Dashboard which we will see later.
Next the DHT11 Sensor takes its action.
The DHT11 Sensor Takes the Input of Humidity and sends the analog input to the ESP32 Module.
The Module will communicate with the cloud through internet and displays the values in the Dashboard.
The ESP32 Module based on the trigger level, sends the output signals to the relay module.
The Relay receives the output signal from ESP32 and turns On/Off the Pump Motor.
The ESP32 plays major role in transferring the data from the sensors and sends back to cloud.
The Module can send the data to the user from anywhere from the world.

## Slide 31: Source Code
Project Explanation

## Slide 32: Source Code – Libraries and Local Variables

## Slide 33: Source Code – Void Setup

## Slide 34: Source Code – Void Setup

## Slide 35: Source Code – Void Loop

## Slide 36: Source Code – Function printOLED()

## Slide 37: Source Code – Function Pump ON/OFF | Trigger

## Slide 38: Cloud Variables and Functions

## Slide 39: Dashboard
Project Explanation

## Slide 40: Computer Dashboard

## Slide 41: Mobile Dashboard

## Slide 42: Prototype Build
Project Explanation

## Slide 44: How to help Farmers through this Project
Conclusion

## Slide 45: How to help Farmers through this Project

## Slide 46: Final Conclusion
Conclusion

## Slide 47: Final Conclusion

## Slide 48: References
References

## Slide 49: References
https://circuitstate.com/wp-content/uploads/2022/12/ESP32-DevKit-V1-Pinout-Diagram-r0.1-CIRCUITSTATE-Electronics-2.png
https://www.circuitstate.com/pinouts/doit-esp32-devkit-v1-wifi-development-board-pinout-diagram-and-reference/#PNG
https://lastminuteengineers.com/esp32-pinout-reference/
https://www.campuscomponent.com/blogs/post/power-supply-for-espressif-module-with-battery-charger-boost-converter#:~:text=Connecting%20the%20Voltage%20regulator's%20output,Polymer%20Battery%20can%20be%20used.

## Slide 50: Thank You
Project By
Dhinesh Kumar M – 23MIA1102
G V N Kishore – 23MIA1157
Rajaa Sasidharan – 23MIA1174
Shailendra Kumar C S – 23MIA1139